## Slide 1: Final Project
- V0 & Optimization

## Slide 2: Github Repository
https://github.com/tahsd/hsd21_project

## Slide 3: Final Term Project Notification
Term Project V0 & Optimization
  Term Project V0
    Implement 8x8 Matrix-Matrix multiplication accelerator
  Term Project Optimized Version (Optional)
    Optimize your work
Optimization methods
  We suggest three ways to optimize your work : DMA / Quantization / Zero Skipping
  DMA
    It boots data transfer speed between DRAM and BRAM.
  Quantization
    Quantize both your activation and weights to 8-bit integer.
  Zero-Skipping
    Avoid multiplication with zeroes to save computation time

## Slide 4: Optimization (1) Quantization
Modify your SW/HW codes for INT8 quantization.
Upgrade your IP
  Switch 32b DSP with 8b integer multiply-adder
    Recall lab3: multadd IP
  Dataset and CNN model will be given in INT8 format
Report the results
  Performance gain
    Compare computation time between fp32 and INT8 ver.
  Utilization
    After implementation

## Slide 5: Optimization (2) Zero-skip
Modify your SW/HW codes for zero-skipping.
  Reduce zero data operations
    Zero data transmission is redundant
    Zero data calculation is redundant
Report the results
  Performance gain
    Compare computation time between and after each project
  Utilization
    If you modify hardware

## Slide 6: Optimization (3) DMA
Try to build your system with DMA
  Modify the SW codes and HW block design
Report the results
  Performance gain
    Compare computation time between and after each project

## Slide 7: Rules for optimization
You can try more than one optimization,
but do not apply multiple optimizations at the same time.
If you have done quantization & DMA, for example, submit three verions of your work.
  V0 (Baseline)
  V0 + quantization
  V0 + DMA
  You should include the same V0 for all the versions.
Each version of your work will be evaluated independently.

## Slide 8: Schedule
Important schedule
  5/31 : Final exam
  6/2 : Interim submission
  6/19 : Final submission

## Slide 9: Scoring Criteria
Implementation
  Baseline
  Once you succeed any implementation of those optimizing methods, you will get additional score regardless its performance.
Inference time
  Baseline
  You will be scored on the speed gain by using each optimizing method.
Accuracy
  Baseline
  Accuracy should be robust enough to quantization and zero-skipping.
Report

## Slide 10: Report
Explain SW/HW System that you implemented.
It is sufficient to include only project-specific contents.
You must include the results and analysis of your work
  inference time, total_image, accuracy, etc.
If you implement any optimized version, compare the results between V0 and the optimized one and include your analysis in the report.
Your submission should reproduce the same result as in the report.
Either in Korean or in English
# of pages does not matter
PDF only!!

## Slide 11: Final Term Project Notification
Requirements
  Result
    Attach all the HW/SW project folders and the bitstream file for the V0 version.
    If you have implemented optimized ones, attach them additionally. (Refer to Slide 7)
    Attach a video that can show the results
      Below is a description of the scenario in which you take a video
        1. Keep the camera away and make sure your host computer and ZedBoard are all visible
        2. Turn on your ZedBoard
        3. Zoom that camera into the host monitor & start minicom
        4. Run benchmark.sh
    Bitstream file’s name: "<Team_number>_zynq_<Version>.bit" ex) 7_zynq_V0.bit / 7_zynq_dma.bit
    Software code folder name: "<Team_number>_SW_<Version>" ex) 7_SW_V0 / 7_SW_dma,
  - Report
  Result + Report to one .zip file
Upload (.zip) file on ETL
  Submit one (.zip) file
    [Project]name1_name2.zip
    Due: 6/19(SAT) 23:59
    No Late Submission