## Slide 1: Lab 11
Lab 11: DMA (Direct Memory Access)

## Slide 2: Lab 11: Overview
Analysis
  Performance measurement tips) time, gettimeofday()
Performance Tuning
  memcpy, DMA
Report
  DUE: 6월 2일 (수) 23시 59분

## Slide 3: Analysis
[Linux Debugging and Performance Tuning: Tips and Techniques, 2005]
  Profiling tools
    stopwatch, date, time, clock, gettimeofday, gprof, kprof, …
zed@debian-zynq:~/lab9$ time sudo ./a.out
real 0m0.054s // elapsed real time
user 0m0.040s // total CPU time in user mode
sys 0m0.000s // total CPU time in kernel mode
#include <sys/time.h>
struct timeval start, finish;
int main()
{
gettimeofday (&start, NULL);
/* … */
gettimeofday (&finish, NULL);
//msec = finish.tv_sec * 1000 + finish.tv_usec / 1000;
//msec -= start.tv_sec * 1000 + start.tv_usec / 1000;
}

## Slide 4: Performance Tuning

## Slide 5: Performance Tuning 1. MEMCPY
memcpy: copy block of memory
  void * memcpy ( void * destination, const void * source, size_t num );
    destination: pointer to the destination array
    source: pointer to the source of data to be copied
    num: number of bytes to copy
gettimeofday (&st[2], NULL);
// memory load
for (i = 0; i < SIZE * (SIZE + 1); i++)
{
*(fpga_bram + i) = flat[i];
}
gettimeofday (&st[3], NULL);
-> 852us
gettimeofday (&st[2], NULL);
// memory load
memcpy( fpga_bram, flat, 16640 );
gettimeofday (&st[3], NULL);
-> ?

## Slide 6: 2. DMA – Block Design
Tutorial on Direct Memory Access
Create a Vivado project and run block_design_dma.tcl
Create HDL Wrapper / Generate Bitstream file
Central DMA
BRAM
DRAM

## Slide 7: DMA – Programmer’s Perspective
BRAM is @ 0x4000_0000 (by PS) and 0xC000_0000 (by CDMA)
  CDMA operation (PG034)
    Assign source address (SA)
    Assign Destination address (DA)
    Assign bytes to transfer (BTT)
    Poll if the operations is done (CDMASR.IDLE)
BRAM ADDR by PS
BRAM ADDR by CDMA

## Slide 8: DMA – New Bootloader
Update the boot loader to enable non-cacheable DRAM
  Switch u-boot.img with u-boot.img.nc
  mv u-boot.img.nc u-boot.img
  Ref) cat /proc/meminfo
DRAM ADDR SPACE
BRAM ADDR SPACE
DRAM running Kernel
Non-Cacheable DRAM
0x1000_0000
0x4000_0000

## Slide 9: DMA – Application
Run a sample c-code to execute DMA operation
  BOARD$ git clone https://github.com/tahsd/hsd21_lab11.git
  BOARD$ make
DRAM ADDR SPACE
BRAM ADDR SPACE
DRAM running Kernel
Non-Cacheable DRAM
// 1. MCPY
gettimeofday (&st[2], NULL);
memcpy( ps_dram, flat, SIZE * (SIZE + 1) * sizeof(float) );
gettimeofday (&st[3], NULL);
1. MCPY
2. DMA

## Slide 10: DMA – Application
Run a sample c-code to execute DMA operation
DRAM ADDR SPACE
BRAM ADDR SPACE
DRAM running Kernel
Non-Cacheable DRAM
1. MCPY
2. DMA
// 2. DMA
gettimeofday (&st[2], NULL);
*(fpga_dma+6) = 0x10000000; // SA
*(fpga_dma+8) = 0xC0000000; // DA
*(fpga_dma+10) = SIZE * (SIZE + 1) * sizeof(float); // BTT
while ((*(fpga_dma+1) & 0x00000002) == 0); // CDMASR.IDLE
gettimeofday (&st[3], NULL);

## Slide 11: Main Practice

## Slide 12: Practice
Follow tutorial & understand the DMA functionality
  Run a given block design in your FPGA
    Run and understand DMA function
  Refer to the CDMA product guide and analyze the main code
  In our term project optimization, you will modify the block design
    Term project = PS + BRAM + Connectivity + Custom IP (MM multiplier) + CDMA
Compare data transfer using CDMA versus transferring data through CPU
  You should modify main.c for transferring data through CPU.

## Slide 13: Homework
Requirements
  Result
    Attach a screenshot of main.c result with [student_number, name]
  Report
    Write down all the points mentioned on the previous page
    In your own words
    Either in Korean or in English
    # of pages does not matter
    PDF only!!
  Result + Report to one .zip file
Upload (.zip) file on ETL
  Submit one (.zip) file
    zip file name : [Lab11]name.zip (ex : [Lab11]홍길동.zip)
  Due: 6/2(WED) 23:59
    No Late Submission